## Slide 1
WEEK 05 / START HERE
HOW DOES THE INTERNET GET FROM HERE TO THERE?
From one browser tap to a world of devices, networks, routers, and servers.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 01
EXPLORER
BUILDER
ENGINEER / RESEARCHER
YOUR DEVICE → LOCAL NETWORK → ISP → OTHER NETWORKS → WEBSITE / SERVICE
WHAT YOU NEED
Paper and a pencil. A phone is optional. No login, downloads, or new equipment.
WHAT YOU WILL MAKE
A labeled route map and a simple packet-delivery experiment you can explain to a friend.
One familiar action; many connected systems. Learn it without needing a computer.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Week 5 is independent of attendance. Learners can pause and work through the deck alone. Core reading 15-20 minutes; paper activity 10-15 minutes; optional advanced tasks afterward.

## Slide 2
WEEK 05 / START HERE
How to use this public lesson
Complete every step independently, or pause and discuss as a group.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 02
EXPLORER
Explain what the internet does and draw how one website reaches a phone.
BUILDER
Simulate packet routes, spot a failure, and design a more resilient path.
ENGINEER / RESEARCHER
Question addressing, forwarding tables, caching, route changes, and measurement.
STOP / DRAW / TEST whenever a challenge appears. A successful lesson produces an answer, an artifact, a next step, or a better question.
No age gate, technical prerequisites, or paid equipment. Continue at your own pace.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Do not use Explorer/Builder/Engineer as fixed labels of people. They are different resolutions of the same topic. Explain abbreviations on first use.

## Slide 3
WEEK 05 / BIG PICTURE
Five weeks, one connected story
Each Thursday increases the resolution of a familiar technology experience.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 03
1
WEEK 1
Technology is a system, not a screen.
2
WEEK 2
A tap travels from input to feedback.
3
WEEK 3
Performance shapes human experience.
4
WEEK 4
Hardware and software cooperate inside a device.
5
WEEK 5
Networks connect devices to services beyond them.
Today: follow the data outside the device and back again.
Notes: INSTRUCTOR / SELF-STUDY NOTES
One sentence recap for each earlier week; skip if audience starts from Week 5. This deck remains standalone.

## Slide 4
WEEK 05 / CORE LESSON
A normal moment: open a website
Imagine entering gunnchos.com in a browser. You expect a page, not a lesson in networking.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 04
WHAT YOU NOTICE
1. You type a readable name.
2. The browser begins loading.
3. Text and images appear.
4. You can interact with the page.
WHAT MUST EXIST
Your device + a local connection + a way to find the site + networks that can forward data + a service that responds + software that renders the result.
Guiding question: how do little pieces of information find the right destination?
Notes: INSTRUCTOR / SELF-STUDY NOTES
An example domain is used for familiarity, not as a promise that a particular page will load or that every request travels to one physical server.

## Slide 5
WEEK 05 / CORE LESSON
The internet is not the same as the web
The internet carries many kinds of communication. The web is one service built on it.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 05
INTERNET = INFRASTRUCTURE
A worldwide network of networks: connected devices and systems exchanging data using common protocols.
WEB = ONE APPLICATION FAMILY
Web browsers use web protocols (like HTTP/HTTPS) to request pages and resources. Email, games, and calls also use the internet.
The web uses the internet; not everything on the internet is a web page.
Quick check: is a video call over the internet necessarily “the web”? No.
Notes: INSTRUCTOR / SELF-STUDY NOTES
MDN: https://developer.mozilla.org/en-US/docs/Learn_web_development/Howto/Web_mechanics/How_does_the_Internet_work . Some calls may run in browsers, but internet and web are distinct concepts.

## Slide 6
WEEK 05 / CORE LESSON
The route at a glance
This is a conceptual map; real routes and service locations vary.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 06
1
YOUR DEVICE
2
Wi-Fi / CELL
3
LOCAL GATEWAY
4
ISP
5
NETWORKS
6
SERVICE
The information also needs a route back. Requests and responses may traverse different paths.
A local Wi-Fi connection does not by itself guarantee access to the internet.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Wireless is one access method; Ethernet also works. Gateways combine multiple functions in consumer routers. Route directions can be asymmetric.

## Slide 7
WEEK 05 / CORE LESSON
Client asks. Server or service responds.
A browser is a client when requesting web content. A website may depend on many services.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 07
CLIENT: MAKES A REQUEST
“Please send the resource at this web address.”
Example: browser on a phone.
SERVER / SERVICE: ANSWERS
Receives a request and returns data or an error. Content may come from nearby caches.
REQUEST
RESPONSE
Websites often include several requests for images, styles, scripts, and data.
Notes: INSTRUCTOR / SELF-STUDY NOTES
MDN: https://developer.mozilla.org/en-US/docs/Web/HTTP/Guides/Overview . Simplified client/server roles, not a claim there is just one server.

## Slide 8
WEEK 05 / CORE LESSON
Before the internet: the local network
Wi-Fi connects you to a local access point. Another connection carries traffic farther.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 08
PHONE / LAPTOP
Runs the browser and joins Wi-Fi or a mobile network.
ACCESS POINT / ROUTER
Connects local devices. A home box may combine Wi-Fi, routing, switching, and modem functions.
PROVIDER CONNECTION
A cable, fiber, cellular, fixed wireless or other access path reaches a network provider.
Try asking: what can still work locally if your internet service is down?
Notes: INSTRUCTOR / SELF-STUDY NOTES
A device can be Wi-Fi associated even when its gateway or upstream ISP is unavailable; some peer-to-peer local traffic may still work.

## Slide 9
WEEK 05 / CORE LESSON
The internet is a network of networks
Your provider connects to other networks; no single router holds the entire internet.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 09
YOUR NETWORK
A home, school, business, or mobile network.
ISP
An internet service provider moves traffic onward.
OTHER NETWORKS
Transit networks, peers, content providers, and CDNs.
DESTINATION SERVICE
The endpoint or cache that returns the resource.
The internet is cooperative routing between independently operated networks.
Notes: INSTRUCTOR / SELF-STUDY NOTES
No one owns the internet end to end. Different network operators connect via peering or transit arrangements. Avoid presenting a fixed single physical chain as universal.

## Slide 10
WEEK 05 / CORE LESSON
Names, addresses, and destinations
Humans remember names. Networks forward packets toward IP destinations.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 10
DOMAIN NAME
gunnchos.com
A human-friendly name. It can map to different addresses over time or location.
DNS LOOKUP
Domain Name System (DNS) helps find the addresses a service advertises.
IP ADDRESS
A numerical network-layer address used for routing, such as 203.0.113.7*
*203.0.113.7 is an example-only documentation address, NOT the real IP of gunnchos.com.
DNS is an address lookup, not the act of downloading the web page.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Use reserved documentation addresses only, not a purported real site address. RFC 5737 documents 203.0.113.0/24 for examples. DNS may return multiple records or CDN-related locations.

## Slide 11
WEEK 05 / CORE LESSON
How DNS helps find a site
Commonly, a cached answer is used; otherwise a resolver looks up the answer.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 11
A
BROWSER
Needs an address
B
LOCAL / RESOLVER CACHE
Can it reuse a recent answer?
C
DNS RESOLVER
Asks DNS infrastructure if needed
D
ADDRESS RESULT
Returns record(s) or an error
A cached answer may skip additional lookups. DNS answers can change and may list multiple addresses.
Different task: “find the address” vs “contact the service.”
Notes: INSTRUCTOR / SELF-STUDY NOTES
DNS does not guarantee that server will answer. HTTPS DNS transports vary, and resolvers/cache behavior vary by system. https://www.cloudflare.com/learning/dns/what-is-dns/

## Slide 12
WEEK 05 / CORE LESSON
Packets: data travels in manageable pieces
An application can transfer data as many network packets, not one giant message.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 12
REQUEST / RESPONSE DATA
PACKET A
address + content
PACKET B
address + content
PACKET C
address + content
PACKET D
address + content
Packets carry addressing and control information, along with some of the data.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Network packets consist of headers and payloads, subject to protocol and MTU. This is a conceptual model, not that every individual web object splits into exactly four equal parts.

## Slide 13
WEEK 05 / CORE LESSON
Do packets arrive perfectly? Not always.
Networks can delay, drop, or deliver packets out of order; the application uses suitable protocols to cope.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 13
ADDRESSING
An IP destination tells routers where a packet should be forwarded.
FORWARDING
Each router selects a next hop using its routing/forwarding information.
DELIVERY RECOVERY
Protocols and applications determine how missing or out-of-order data is handled.
Packet paths may differ. Reassembly and reliability depend on transport/application behavior.
Notes: INSTRUCTOR / SELF-STUDY NOTES
TCP and QUIC provide reliable streams; UDP alone does not. Do not claim every IP packet inherently receives an acknowledgement or that every packet follows the same path.

## Slide 14
WEEK 05 / CORE LESSON
What does a router actually do?
Think “Which neighbor should receive this packet next?” rather than a global GPS map.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 14
INPUT
Packet arrives with a destination IP address.
DECISION
Forwarding table chooses a next hop or an outgoing interface.
OUTPUT
The router forwards, or may discard it when forwarding is not possible.
Routers usually decide the NEXT STEP, not the entire end-to-end route.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Routing protocols and policies influence forwarding tables. Avoid suggesting routers independently discover a path for each packet globally.

## Slide 15
WEEK 05 / CORE LESSON
One destination, more than one possible path
A simplified teaching network shows why alternative routes can matter.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 15
D
H
A
B
S
C
E
PRIMARY PATH: D → H → A → B → S
ALTERNATE: D → H → A → C → E → S
Route changes are possible, not automatic or immediate: policies and available paths matter.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Diagram is fictitious. Shows two potential paths for paper game. Node labels D=device, H=home router, A=provider router, B/C/E=other routers, S=service. Path selection can be asymmetric and may vary by route policy.

## Slide 16
WEEK 05 / CORE LESSON
HTTP: asking for a resource
The browser asks a service for a page or asset and interprets what comes back.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 16
1. REQUEST
A web client requests a resource by URL and method, often GET.
2. RESPONSE
A server, CDN, or service sends a status and content or error.
3. RENDER
The browser processes HTML, styles, scripts, images, and more.
Web protocols evolve: HTTP/1.1 and HTTP/2 commonly use TCP; HTTP/3 uses QUIC.
Notes: INSTRUCTOR / SELF-STUDY NOTES
MDN HTTP overview, HTTP/3 with QUIC. Not all web browsing uses just a single GET; pages may have many subrequests, caching, cookies, redirections and service workers.

## Slide 17
WEEK 05 / CORE LESSON
HTTPS: protect what travels
HTTPS usually encrypts communication between the client and the authenticated endpoint.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 17
WHAT IT HELPS WITH
Encryption and integrity protect content in transit from many on-path observers. Certificate checks help authenticate the server connection.
WHAT IT DOES NOT GUARANTEE
A site can still be malicious, a password can still be stolen by scams, and some connection metadata may remain observable.
Good habit: check the address, avoid sharing passwords, and never post private account details.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Teach safe browsing. HTTPS protects a transport connection, not trustworthiness of site content. DNS encryption and visibility vary. Never collect learner credentials.

## Slide 18
WEEK 05 / CORE LESSON
The whole web journey, in seven moves
This is a conceptual common case; some steps may use cache or differ by protocol.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 18
1
TYPE NAME
2
FIND ADDRESS
3
CONNECT
4
SEND REQUEST
5
ROUTE PACKETS
6
GET RESPONSE
7
DISPLAY
A page may need several requests and components. It might be served from a nearby cache.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Distinguish DNS lookup, connection establishment (including security), HTTP, return data, rendering. Browser caching and CDN endpoints alter real sequences.

## Slide 19
WEEK 05 / CORE LESSON
When it fails, ask WHERE in the journey
Different symptoms are clues, not proofs of a specific cause.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 19
Wi-Fi connected, pages never load
Could be gateway / DNS / ISP / remote service.
One website fails; others work
Could be site, DNS entry, account, or browser issue.
Some pages load, others are slow
Could be large assets, congestion, caching, or device limits.
A video call freezes; email works
Could be real-time sensitivity, jitter, loss, or app behavior.
Observe → locate → test → learn. Do not jump from symptom to certainty.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Some troubleshooting requires professional/school IT support. Safe user checks only; no credential collection or active scanning of others.

## Slide 20
WEEK 05 / PAPER LAB
Your hands-on task: deliver three packets
You can complete this entire activity with pencil and paper in 10 minutes.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 20
WHAT TO DRAW
Copy the network on the next slide. Make three little paper messages: P1, P2, P3. Give them a source D and destination S.
RULES
Move a packet only along drawn links. Use route D–H–A–B–S while B works. Later, pretend B fails. Find another available path.
WRITE DOWN: which routers were visited, number of links, and what you changed.
Notes: INSTRUCTOR / SELF-STUDY NOTES
If working alone use pencil and arrows; if in a group, people act as routers. No internet or personal data is necessary.

## Slide 21
WEEK 05 / PAPER LAB
Copy this network onto paper
D = Device • H = Home router • A/B/C/E = Routers • S = Service
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 21
D
H
A
B
S
C
E
Goal: get P1, P2 and P3 from D to S; do not jump between unconnected nodes.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Learner worksheet also includes this same map. Edges are conceptual bidirectional links. In real networks paths may be directional by policy and data-plane state.

## Slide 22
WEEK 05 / PAPER LAB
Round 1: everything works
Use the shorter illustrated route for packet P1.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 22
DO THIS
1. Start P1 at D.
2. Move to H, then A.
3. Continue through B to S.
4. Write the full route and count the links.
CHECK BEFORE MOVING ON
Did P1 reach S?
Which nodes did it visit?
How many links did it cross?
What does a router need to decide at A?
PAUSE: write your route before looking at the worked answer.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Expected route D-H-A-B-S, four links. Router A forwards toward B in this teaching example.

## Slide 23
WEEK 05 / PAPER LAB
Round 2: imagine router B goes offline
Route P2 and P3 without visiting B.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 23
CHALLENGE
Cross out B and its connected links. Find another valid D-to-S route. Draw new arrows and count how many links it uses.
DISCUSS
Does another path exist?
Does every real network switch instantly?
What should users see if rerouting causes a delay?
Engineering idea: a backup path helps only if the network knows to use it.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Expected alternative D-H-A-C-E-S, five links. Forwarding policy and convergence can delay or prevent rerouting; alternate paths are not universal guarantees.

## Slide 24
WEEK 05 / PAPER LAB
Worked solution: the path can change
Fictitious paths illustrate a principle; they are not measured internet routes.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 24
ROUND 1: B AVAILABLE
D → H → A → B → S
Four links. The packet follows the illustrated primary route.
ROUND 2: B FAILED
D → H → A → C → E → S
Five links. This alternate route avoids B in the exercise.
Lesson: alternate paths can improve resilience, but may add delay or complexity.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Different number of links does not prove real latency: physical distance, speed, queues, access technology, processing, policies vary.

## Slide 25
WEEK 05 / OPTIONAL PHONE
Observe your network without taking risks
A phone is optional. Do not publish addresses, passwords, Wi-Fi details, or other private information.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 25
1. LOOK
Open your phone’s Wi-Fi or cellular settings. Are you using a local Wi-Fi access point or cellular data?
2. NOTICE
While on Wi-Fi, try a harmless public webpage. Does it load? Can you tell from this alone where a failure might be?
3. RECORD
Write observations, not account details. Example: “Connected to Wi-Fi; public site loads slowly.”
Do not change school/work network settings or run network scans without authorization.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Avoid asking participants to toggle their phone connectivity if they depend on it. No data collection, no screenshots of settings or addresses required.

## Slide 26
WEEK 05 / BUILDER CHALLENGE
Design more reliable access for a community library
The goal is a usable learning experience, not merely a glowing Wi-Fi icon.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 26
THE PROBLEM
The library has Wi-Fi, but learners report slow pages and occasional outages during busy hours. Devices vary and some learners use phones only.
YOUR DESIGN
Draw device → Wi-Fi → gateway → ISP → service. Mark three possible failure points. Propose one low-cost improvement and one way to test it.
What evidence would help distinguish coverage, capacity, DNS, and remote-site problems?
Notes: INSTRUCTOR / SELF-STUDY NOTES
Do not claim Wi-Fi or extra routers always solve congestion; measure before interventions. Choose accessible, cost-conscious solutions.

## Slide 27
WEEK 05 / ENGINEER / RESEARCHER
Increase the resolution: five deeper questions
Advanced options support deeper inquiry without being prerequisites for beginners.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 27
1
DNS CACHE
When can a cached answer help? When might it become stale?
2
ROUTING POLICY
How do networks choose next hops and respond to failures?
3
TRANSPORT
When do TCP and QUIC differ? What reliability do they provide?
4
MEASUREMENT
What can ping or traceroute reveal—and what can’t they prove?
5
SECURITY / PRIVACY
What does HTTPS protect? What metadata or threats remain?
State your assumption, define an observation, test, and report limitations.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Internet BGP chooses reachability/policy between autonomous systems, not necessarily fewest hops. Traceroute may omit/filter hops. HTTP/3 uses QUIC over UDP; 1.1/2 typically TCP. No participant network scanning.

## Slide 28
WEEK 05 / CHECK YOURSELF
Four questions to test your map
Try your answers BEFORE moving to the next slide.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 28
1. Is Wi-Fi access exactly the same as internet access?
2. Does DNS download a webpage, or help find an address?
3. What is a router’s immediate forwarding decision?
4. If a route fails, will every packet instantly find a new route?
Pause and answer in your own words. You need no special terminology.
Notes: INSTRUCTOR / SELF-STUDY NOTES
These checks are included in public deck for independent learners.

## Slide 29
WEEK 05 / CHECK YOURSELF
Answers: follow the evidence
An explanation is more important than memorizing a definition.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 29
1
1. NO
Wi-Fi connects local devices. The gateway or provider can still be unavailable.
2
2. ADDRESS
DNS helps resolve names to DNS records such as IP addresses; HTTP fetches resources.
3
3. NEXT HOP
A router uses destination information and a forwarding table to choose where to send a packet next.
4
4. NO GUARANTEE
An alternate path, routing state, and sufficient time are needed; some traffic may fail.
You now have a route map, a failure scenario, and an evidence-based explanation.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Emphasize why each false assumption is tempting. A strong connection bar/green Wi-Fi icon indicates only part of the system.

## Slide 30
WEEK 05 / TAKEAWAY
One webpage. Many networks. One human experience.
Use the five questions below whenever a digital experience breaks or surprises you.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 30
WHO?
Which device or client is asking?
WHERE?
What address or service is being contacted?
HOW?
Which local and provider networks carry the data?
WHAT?
What request and response travel?
WHY NOT?
Which boundary may be failing or slow?
NEXT WEEK / NOV 5: How does AI actually produce an answer?
Notes: INSTRUCTOR / SELF-STUDY NOTES
Invite learners to share their packet route sketch, without screenshots containing private device or network details. Optional Twitch / Instagram sharing.

## Slide 31
WEEK 05 / CONTINUE LEARNING
Read, build, and share the route map
Free public links. Illustrative diagrams; actual network paths and services differ.
THURSDAY TECHNOLOGY OPEN LAB | ASK • LEARN • BUILD | gunnchos.com
W05 / 31
gunnchOS3k / PROGRAM
https://gunnchos.com
WAIKE / LEARNING PATHS
https://github.com/gunnchOS3k/waike-research-ops
THE TECHNOLOGY LANDSCAPE
https://github.com/gunnchOS3k/gunnchos-technology-landscape
MDN / HOW THE INTERNET WORKS
https://developer.mozilla.org/en-US/docs/Learn_web_development/Howto/Web_mechanics/How_does_the_Internet_work
MDN / HOW THE WEB WORKS
https://developer.mozilla.org/en-US/docs/Learn_web_development/Getting_started/Web_standards/How_the_web_works
CLOUDFLARE / DNS BASICS
https://www.cloudflare.com/learning/dns/what-is-dns/
MDN / HTTP-3 & QUIC
https://developer.mozilla.org/en-US/docs/Glossary/QUIC
Questions are valuable: share what surprised you and what you want to build.
Notes: INSTRUCTOR / SELF-STUDY NOTES
Public educational materials for individual learning and community presentations. References: MDN & Cloudflare. Week 5 focuses on conceptual correctness and teaches sample routes without claiming any actual live network measurement.